2X8D Sequencer Performance Specification
A Synthesizer Module

Block Diagram

~35 GPIO
DAC may need an amp before the output
Signal Description
Step Select	Turn on to insert this step into the sequence. If on, a gate output and trigger are generated for this step.
Sequence Length	Can set from 1 to 8. If set to 6, the 6th step is the last one in the sequence. Then the sequence either stops or resets.
CV Level	Controls the CV value during this step
Reset	Sets the sequence back to the first step
Pause	Pressing and letting go causes the sequencer to pause. Pressing again causes it to start.
Series/Parallel Select	Configure the sequencer as either 2x8 step sequencers, or 1x16 sequencer.
Stop/Repeat Sequence	Stop: When the sequence is at the end, stop it / Repeat: when the sequence is at the end, start again from the beginning.
Exact Time Select	Unpressed: Clock Rate is incremented in as fine steps as possible. When held, is adjusted in steps of something like 1/16 or 1/8 seconds. When pressed, rounds current clock rate to nearest round increment.
Clock Rate	How fast the sequence changes steps.
Step Indicator	Turns on when its step is active. If its step select is off, the LED doesn’t turn on.
CV out	Outputs a voltage that changes each step based on the CV level pots. Does it go to 0 if step select is off?
Gate output	Stays high until a step is not active.
Trig output	Goes high for every active step for a very short time, something like 1ms

Possible Parts
Part	Digi-Key PN	MFG	MFG PN	Cost	Q
ADC	MCP3208-CI/SL-ND	Micro	MCP3208-CI/SL	5.24	2
DAC	296-DAC70501MDGSRCT-ND	TI	DAC70501MDGSR	6.99	2
	296-46082-1-ND	TI	DAC8552IDGKR	10.61	1
8:3 Encoder	296-26468-1-ND	TI	SN74HC148DR	0.62	4
3:8 Decoder	296-24353-1-ND	TI	CD74HC238M96	0.66	2
5V Ref	LM4120AIM5-5.0/NOPBCT-ND	TI	LM4120AIM5-5.0/NOPB	3.19	1

Possible Features
Found on: https://www.tomleemusic.ca/169264
- Add a third option to step select: On = gate and trig generated, Off = gate and trig not generated, Skip = step is taken out of the sequence completely so if you want to remove a step you don’t have to retune every step after it.
- second 8 step sequencer sets individual gate length of the first 8 step sequencer (in addition to parallel and sequencer modes)
- several running directions: forward, backward, random
- CV scaling: 1V/octave
- several CV output ranges: 1V, 2V, 5V, 8V (1, 2, 5, and 8 octaves)
- Exact note select: let’s you tune the CV out to exact notes if selected. Maybe set it to 1/16 of a second steps? Can I make the steps larger if the encoder is turned faster?